## Slide 1
1/6
BSc THESIS · ZERO PRESENTATION
Implementation of Label-Free Teacher–Student Commissioning for Vibration-Signal-Based Fault Detection
Ata Göker
Supervisor: dr hab. inż. Rafał Zdunek
Wrocław University of Science and Technology · Faculty of Electronics, Photonics and Microsystems
Notes: Hello, everyone. My name is Ata Göker, and my engineering thesis is titled: Implementation of Label-Free Teacher–Student Commissioning for Vibration-Signal-Based Fault Detection. My supervisor is dr hab. inż. Rafał Zdunek. In the next six minutes I will explain the problem, the core idea, what I plan to build, the literature I rely on, and where I am now.

## Slide 2
The problem: domain shift
Zero presentation · Ata Göker
2/6
LAB · SOURCE
Labeled
Known healthy and faulty recordings
domain shift
NEW MACHINE · TARGET
Unlabeled
Different load, speed, mounting
Labeling every new installation is too slow and too expensive
Can the model adapt using only unlabeled data from the new machine?
Notes: Let me start with the problem. Machine learning models can detect bearing faults from vibration signals very well in the laboratory, where we know exactly which recordings are healthy and which are faulty. But when the same model is installed on a new machine, conditions change: a different load, a different shaft speed, a different mounting. The vibration signals shift, and the model can lose accuracy. This is called domain shift. The obvious fix is to collect and label new data for every installation. But that costs time and money, and on a freshly installed machine the true condition is simply not known. So my question is: can the model adapt using only unlabeled data from the new machine?

## Slide 3
The idea: teacher–student adaptation
Zero presentation · Ata Göker
3/6
1
Teacher predicts
A slow average of the student labels each unlabeled window. Only confident predictions are kept.
2
Student learns
Uses lab labels, accepted pseudo-labels, and stable predictions under small signal changes.
3
Teacher updates
Teacher weights follow the student by exponential moving average. Then repeat.
Risk to study: a confident pseudo-label can still be wrong.
Notes: My answer is a teacher–student scheme. The student is a neural network first trained on labeled laboratory data. The teacher is a slowly moving average of the student's weights, so its predictions are more stable. On the new machine, the teacher looks at each unlabeled vibration window and produces a provisional label, called a pseudo-label. If its confidence is above a threshold, for example ninety percent, the label is accepted. The student then learns from three things: the lab data, the confident pseudo-labels, and a consistency requirement, meaning that a slightly changed version of the same signal should get the same prediction. Then the teacher is updated, and the loop repeats. One important risk, which I will study, is that a confident prediction can still be wrong, and learning from wrong labels can reinforce mistakes.

## Slide 4
What I will build
Zero presentation · Ata Göker
4/6
DATA
CWRU vibration signals
Raw 1D signals cut into short windows.
BASELINE
CNN, 4 classes
Healthy, inner-race, rolling-element, outer-race.
ADAPTATION
Teacher–student loop
EMA teacher with confidence-based pseudo-labels.
EVALUATION
Zero target labels
Used only for the final test, never in training.
Notes: Here is what I will build. First, I will process raw one-dimensional vibration signals from the standard CWRU bearing dataset, cutting them into short windows. Second, a baseline convolutional neural network for four classes: healthy, inner-race fault, rolling-element fault and outer-race fault. Third, the teacher–student adaptation loop. And fourth, just as important, a strict evaluation protocol: no target labels are used during adaptation or model selection. They are used only at the end, to measure the result honestly. I will compare the adapted models with the baseline and with simpler alternatives. The goal is not guaranteed improvement, but credible evidence of when adaptation helps and when it fails.

## Slide 5
Key literature
Zero presentation · Ata Göker
5/6
2024
Forest & Fink
Sensors 24(23), 2024
Calibrated Adaptive Teacher: main method reference
2024
Yu et al.
Reliab. Eng. Syst. Saf. 248, 2024
Source-free adaptation: deployment without source data
2017
Tarvainen & Valpola
NeurIPS 2017
Mean Teacher: the weight-averaged teacher
2015
Smith & Randall
Mech. Syst. Signal Process., 2015
CWRU benchmark study: data anomalies
Teal: papers selected with my supervisor
Notes: I rely on four main sources. The first two were selected with my supervisor. Forest and Fink, 2024, in Sensors, present the Calibrated Adaptive Teacher. It combines teacher–student self-training with calibrated confidence, and its public code is my closest implementation reference. It still uses source data during adaptation, so it is not source-free. Yu and colleagues, 2024, in Reliability Engineering and System Safety, study source-free adaptation, where the original data is not available at deployment. This motivates the commissioning scenario. Tarvainen and Valpola, 2017, introduced Mean Teacher, the weight-averaging idea behind my teacher. Finally, Smith and Randall, 2015, analyze the CWRU data and its anomalies, which tells me how to handle the dataset carefully.

## Slide 6
State of progress
Zero presentation · Ata Göker
6/6
DONE
Theoretical groundwork and literature review
Experimental matrix and evaluation protocol
IN PROGRESS
Python / PyTorch environment setup
NEXT
Verify raw CWRU data
Code the baseline CNN
Add the teacher–student loop
No models trained yet; results will follow.
Notes: Progress so far: I have completed the theoretical groundwork and the literature review, and I have defined the experimental matrix and the evaluation protocol. I am currently setting up the Python and PyTorch environment. The next steps are to verify the raw CWRU data, implement the baseline CNN, and then add the teacher–student loop. No models have been trained yet, so I have no results to report today. Thank you for listening. I am happy to take questions.